## Slide 1: Lane Detection
Day 2 - Morning Session 1

## Slide 2: Image Pixels
Pixel is considered the “color” or the “intensity” of light that appears in a given place in our image.
Range of 0 to 255
Pixels are represented in two ways:
  Grayscale/Single channel
  Color

## Slide 3: Grayscale/Single channel
Each pixel has value between 0 and 255 where "0" corresponds to black and "255" being white

## Slide 4: Color(RGB/HSV/HSL)
RGB
  Each of the red, blue, green channel is represented by integer.
  [255,255,255] is white color
  [0,0,0] is black color
  [255,0,0] is pure red color
  [0,0,255] is pure blue color
  https://www.w3schools.com/colors/colors_rgb.asp

## Slide 5: Color
HSV
  Hue is the color portion of the model, expressed as a number from 0 to 360 degrees.
  Saturation describes the amount of gray in a particular color, from 0 to 100 percent. Reducing this component toward zero introduces more gray and produces a faded effect.Value describes the brightness or intensity of the color, from 0 to 100 percent, where 0 is completely black, and 100 is the brightest and reveals the most color.
  For HSV, Hue range is [0,179], Saturation range is [0,255] and Value range is [0,255]
https://math.hws.edu/graphicsbook/demos/c2/rgb-hsv.html
https://opencv24-python-tutorials.readthedocs.io/en/latest/py_tutorials/py_imgproc/py_colorspaces/py_colorspaces.html

## Slide 7: Image Size

## Slide 8: Image Array

## Slide 9: Image Distortion
Some pinhole cameras introduce significant distortion to images.
Two major kinds of distortion:
  Radial distortion
  Tangential distortion
  Reference: https://medium.com/@vivanraaj/perception-in-self-driving-cars-part-1-1ccca42b169

## Slide 10: Radial Distortion
Cause straight lines to be appear curved
Becomes larger the farther points are from the center of the image

## Slide 11: Radial Distortion

## Slide 12: Tangential Distortion
Occurs when the image-taking lense is not aligned perfectly parallel to the imaging plane
Some areas in the image may look nearer than expected.

## Slide 13: Tangential Distortion

## Slide 14: Region of Interest
Portion of an image that you want to filter or operate on in some way.
You can represent an ROI as a binary mask image.
In the mask image, pixels that belong to the ROI are set to 1 and pixels outside the ROI are set to 0 .

## Slide 15: Original Image and Flipped Image

## Slide 16: Undistorted Image and RGB image

## Slide 17: ROI Image and Green mask Image

## Slide 18: Grayscale Image

## Slide 19: Final X and Y value